## Slide 1
Basic Theorems
prove by truth table
For equality proof, F1=F2, for all possibility in the input variables (all rows), both side of equation must have equal value for same input variables.
For inequality proof, F1≠F2, find at least one possibility (a row) that have different values.

## Slide 2
Basic Theorems
Prove by postulates

## Slide 3
X + X = X
X+ X + X + … + X = X

## Slide 4
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1

## Slide 5
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property

## Slide 6
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property
= X + (XX’) using distributive property of + over ×

## Slide 7
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property
= X + (XX’) using distributive property of + over ×
= X + 0 using complement property

## Slide 8
X + X = X
X+ X + X + … + X = X
X + X =
= (X + X) 1 using identity e×=1
= (X + X) (X+X’) using complement property
= X + (XX’) using distributive property of + over ×
= X + 0 using complement property
= X using identity property of e+=0

## Slide 9
X + 1 = 1
X+ Y + Z + … + 1 = 1

## Slide 10
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1

## Slide 11
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property

## Slide 12
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property
= X + (1X’) using distributive property of + over ×

## Slide 13
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property
= X + (1X’) using distributive property of + over ×
= X + X’ using identity e×=1

## Slide 14
X + 1 = 1
X+ Y + Z + … + 1 = 1
X + 1 =
= (X + 1) 1 using identity e×=1
= (X + 1) (X+X’) using complement property
= X + (1X’) using distributive property of + over ×
= X + X’ using identity e×=1
= 1 using complement property

## Slide 15
X + xy = x
X + xY + xZW + … + xwAD = x
Absorption

## Slide 16
X + xy = x
X + xY + xZW + … + xwAD = x
X + xy =
= X1+XY using identity e×=1
= x(1 + Y) using distributive property of × over +
= X1 using previous theorem x+1=1
= X using identity e×=1
Absorption

## Slide 17
duality
    Dual(F) = OR AND, 1 0
    Dual(F) may or may not equal to F!

## Slide 18
duality
X+1 X0
X+X’ XX’
(X+Y)’ (XY)’

## Slide 19
Duality
For Complement (NOT)

## Slide 20
F=A+(BC) → F’=[A+(BC)]’=[A’(BC)’]=[A’(B’+C’)]
Duality
For Complement (NOT)

## Slide 21
F=A+(BC) → Dual(F) → A(B+C) → F’=A’(B’+C’)
Duality
For Complement (NOT)

## Slide 22
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
F’ = [AB(C+(DL’G(B’+A+E)))(H+(J’A’B))]’
F’ = [AB(…)(H+(J’A’B))]’
F’ = [A’+B’+(…)’+(H+(J’A’B))’]
F’ = [A’+B’+(…)’+(H’(J’A’B)’)]
F’ = [A’+B’+(…)’+(H’(J+A+B’))]
F’ = [A’+B’+(C+(…))’+(H’(J+A+B’))] OMG!

## Slide 23
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A

## Slide 24
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+

## Slide 25
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+B

## Slide 26
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+B+(

## Slide 27
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+B+(C

## Slide 28
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+B+(C(

## Slide 29
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+B+(C(D+L’+G+(B’AE)))(H(J’+A’+B))

## Slide 30
F = AB(C+(DL’G(B’+A+E)))(H+(J’A’B))
What’s F’?
Dual(F) = A+B+(C(D+L’+G+(B’AE)))(H(J’+A’+B))
Complement all variables only!
F’ = A’+B’+(C’(D’+L+G’+(BA’E’)))(H’(J+A+B’))

## Slide 31
Duality Theorem
A postulate or a proved theorem for F, also a postulate or a proved theorem for Dual(F)

## Slide 32
duality
{X+1=1} {X0 = 0}
{X+X’=1} {XX’=0}k
{(X+Y)’=X’Y’} {(XY)’=X’+Y’}

## Slide 33
X(x+y) = x
X(x+Y)(x+Z) … (x+w) = x
{X(x+y)= X} {X+XY=X}
We proved the dual version
Using the duality property, this is also true!
Absorption

## Slide 34
Y = AB + A'C + BC
Y = AB + A'C + BC.1
Y = AB + A'C + BC.(A + A’)
Y = AB + A'C + ABC + A’BC
Y = AB(1 + C) + A'C(1 + B)
Y = AB + A’C
F = AB + BC' + AC  F = BC' + AC

## Slide 35
Minimization
Boolean Algebra (algebraically)
aka. Algebraic Manipulation

## Slide 36
Example I

## Slide 37
F = zy’x’+ zYX + Zyx’ + zy’X
4 × 3-input-and
1 × 4-input-OR

## Slide 38
F = zy’x’+ zYX + Zyx’ + zy’X

## Slide 39
F = z (y’x’ + yx + yx’ + y’x)

## Slide 40
F = z (y’x’ + yx + yx’ + y’x)

## Slide 41
F = z (y’(x’+X) + yx + yx’)

## Slide 42
F = z (y’(x’+X) + yx + yx’)

## Slide 43
F = z (y’ 1 + yx + yx’)

## Slide 44
F = z (y’ 1 + yx + yx’)

## Slide 45
F = z (y’ + yx + yx’)

## Slide 46
F = z (y’ + yx + yx’)

## Slide 47
F = z (y’ + y (x+X’))

## Slide 48
F = z (y’ + y (x+X’))

## Slide 49
F = z (y’ + y1)

## Slide 50
F = z (y’+y)

## Slide 51
F = z (y’+y)

## Slide 52
F = z1

## Slide 53
F = z
0 gates!

## Slide 54
Example I
Another Approach

## Slide 55
F = zy’x’ + zyx+ zyx’ + zy’x

## Slide 56
F = zy’ (x’+X) + zyx + zyx’

## Slide 57
F = zy’ (x’+X) + zyx + zyx’

## Slide 58
F = zy’ (x’+X) + zy (x+X’)

## Slide 59
F = zy’ (x’+X) + zy (x+X’)

## Slide 60
F = zy’1 + zy1

## Slide 61
F = zy’ + zy

## Slide 62
F = z (y’+Y)

## Slide 63
F = z1

## Slide 64
F = z
0 gates!

## Slide 65
Example I
Another Approach

## Slide 66
F = zy’x’+ zYX + Zyx’ + zy’X
Absorption?

## Slide 67
Example II

## Slide 68
F = zy’x’ + zyx’ + Z’y’x
3 × 3-input-and
1 × 3-input-OR

## Slide 69
F = zy’x’ + zyx’ + Z’y’x

## Slide 70
F = zx’(y’+Y) + Z’y’x

## Slide 71
F = zx’ (y’+Y) + Z’y’x

## Slide 72
F = zx’1+ Z’y’x

## Slide 73
F = zx’+ Z’y’x
1 × 2-input-and
1 × 3-input-and
1 × 2-input-OR

## Slide 74
Design recap
SoP (ANDs-OR)  NAND
PoS (ORs-AND)  NOR d

## Slide 75
Given two unsigned numbers x and y, design a logic circuit to see

## Slide 76
What is the range of x and y?

## Slide 77
What is the range of x and y?

## Slide 78
What is the range of x and y?

## Slide 79
What is the range of output?

## Slide 80
Y2 | Y1 | X2 | X1 | F(Y2,Y1,X2,X1)=?
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 81
Y2 | Y1 | X2 | X1 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15)
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Y2 | Y1 | X2 | X1 | 
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 82
Y2 | Y1 | X2 | X1 | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Y2 | Y1 | X2 | X1 | 
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 83
Y2 | Y1 | X2 | X1 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1
Y2 | Y1 | X2 | X1 |  | 
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1

## Slide 84
Which design?

## Slide 85
Which design?
SoP and PoS are both effective
SoP and PoS have same efficiency (2-levels)

## Slide 86
Which design?
Cost: How many gates in SoP vs. PoS?

## Slide 87
 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
AND | ? | ?
OR | ? | ?
NOT | ? | ?
NAND | ? | ?
NOR | ? | ?
AND | ? | ?
OR | ? | ?
NOT | ? | ?
NAND | ? | ?
NOR | ? | ?

## Slide 88
 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
AND | Each minterm one 4-input-AND | Each MAXTERM one 4-input-OR
OR | One final 10-input-OR | One final 6-input-AND
NOT | Doesn’t Matter Much | Doesn’t Matter Much
AND | Each minterm one 4-input-AND | Each MAXTERM one 4-input-OR
OR | One final 10-input-OR | One final 6-input-AND
NOT | Doesn’t Matter Much | Doesn’t Matter Much

## Slide 89
 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
AND | 10 ✕ 4-input-AND | 6 ✕ 4-input-OR
OR | 10-input-OR = 3 ✕ 4-input-OR | 6-input-AND = 2 ✕ 4-input-AND
NOT | Doesn’t Matter Much | Doesn’t Matter Much
AND | 10 ✕ 4-input-AND | 6 ✕ 4-input-OR
OR | 10-input-OR = 3 ✕ 4-input-OR | 6-input-AND = 2 ✕ 4-input-AND
NOT | Doesn’t Matter Much | Doesn’t Matter Much

## Slide 90
 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
AND | 10 ✕ 4-input-AND | 6 ✕ 4-input-OR
OR | 10-input-OR = 3 ✕ 4-input-OR | 6-input-AND = 2 ✕ 4-input-AND
NOT | Doesn’t Matter Much | Doesn’t Matter Much
AND | 10 ✕ 4-input-AND | 6 ✕ 4-input-OR
OR | 10-input-OR = 3 ✕ 4-input-OR | 6-input-AND = 2 ✕ 4-input-AND
NOT | Doesn’t Matter Much | Doesn’t Matter Much

## Slide 92
 | F(Y2,Y1,X2,X1)= m(0,1,2,3,5,6,7,10,11,15) | F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
NAND | 10 ✕ 4-input-NAND + 1 ✕ 10-input-NAND | 
NOR |  | 6 ✕ 4-input-NOR + 1 ✕ 6-input-NOR
NAND | 10 ✕ 4-input-NAND + 1 ✕ 10-input-NAND | 
NOR |  | 6 ✕ 4-input-NOR + 1 ✕ 6-input-NOR

## Slide 94
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
OMG!!

## Slide 95
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)

## Slide 96
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)

## Slide 97
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1 (Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)

## Slide 98
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)

## Slide 99
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
Are we done?!

## Slide 100
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) +(Y’2Y1X2X1)
OMG!!

## Slide 101
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) +(Y’2Y1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) + (Y’2Y’1X2X1)

## Slide 102
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) +(Y’2Y1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) + (Y’2Y’1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2(X’1+X1))+(Y’2Y’1X’2X1)

## Slide 103
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) +(Y’2Y1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) + (Y’2Y’1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2(X’1+X1))+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(X2X1Y’2)+(Y’2Y’1X2(1))+(Y’2Y’1X’2X1)
OMG!!

## Slide 104
F(Y2,Y1,X2,X1)= M(4,8,9,12,13,14)
= (M4)(M8)(M9)(M12)(M13)(M14)
= (Y2+Y’1+X2+X1)(Y’2+Y1+X2+X1)(Y’2+Y’1+X2+X1)(Y’2+Y’1+X2+X’1)(Y’2+Y’1+X’2+X1)
Dual  (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2Y1X2X1)+(Y’2Y’1X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(Y1+Y’1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1(1))+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) +(Y’2Y1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2X’1)+(Y’2Y’1X’2X1) + (Y’2Y’1X2X1)
= (Y2Y’1X2X1)+(Y’2X2X1)+(Y’2Y’1X2(X’1+X1))+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(X2X1Y’2)+(Y’2Y’1X2(1))+(Y’2Y’1X’2X1)
= (Y2Y’1X2X1)+(X2X1Y’2)+(Y’2Y’1X2)+(Y’2Y’1X’2X1)
Are we done?! Honestly, I don’t know  

## Slide 105
Minimization
Boolean Algebra (algebraically)
    Needs to be smart. It is hard due to guesswork (which rules to apply?)
    If the number of variables (ABCDEF…) and/or number of minterms (MAXTERMS) grows
    No Algorithm
    Is the result minimal?!

## Slide 106
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation

## Slide 107
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation
Algorithm; Straightforward, up to six variables
Result is always minimal

## Slide 108
Minimization
II) Map (Karnaugh map, K-map)
aka. Graphical Manipulation
Algorithm; Straightforward, up to six variables
Result is always minimal

## Slide 109
Maurice Karnaugh
Physicist
Mathematician
Inventor
Bell Labs (1954)
"The Map Method for Synthesis of
Combinational Logic Circuits”